## Slide 1: Computer Architecture Experiment
Topic 6. Dynamically Scheduled Pipelines using Scoreboarding
浙江大学计算机学院

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of pipelines that support multicycle operations.
Understand the principle of Dynamic Scheduling With a Scoreboard.
Master the design methods of pipelines that support multicycle operations.
Master the design methods of Dynamically Scheduled Pipelines using Scoreboarding.
Master verification methods of Dynamically Scheduled Pipelines using Scoreboarding.

## Slide 4: Experiment Task
Redesign the pipelines with IF/IS/RO/FU/WB stages and supporting multicycle operations.
Design of a scoreboard and integrate it to CPU.
Verify the Pipelined CPU with program and observe the execution of program.

## Slide 6: Status
Status | Wait until | Bookkeeping
Issue (Structural and WAW) | !busy[FU] && !result[RD] | busy[FU] = 1, op[FU] = OP, dst[FU] = RD, src1[FU] = RS1, src2[FU] = RS2, read1[FU] = result[RS1], read2[FU] = result[RS2], wait1[FU] = !read1[FU], wait2[FU] = !read2[FU], result[RD] = FU
Read operands (RAW) | wait1[FU] && wait2[FU] | wait1[FU] = 0, wait2[FU] = 0
Function unit | Function unit completes its work | 
Write back (WAR) | ∀f, !(src1[f] == dst[FU] && wait1[FU] ¦¦ src2[f] == dst[FU] && wait2[FU]) or similarly ∀f, (src1[f] != dst[FU] ¦¦ !wait1[FU]) && (src2[f] != dst[FU] ¦¦ !wait2[FU]) | ∀f, if read1[f] == FU then wait1[f] = 1, if read2[f] == FU then wait2[f] = 1. result[ dst[FU] ] = 0, busy[FU] = 0

## Slide 7: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | Str.(in 2nd round with 60
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | Structural Haz.(0x4)
3 | 004100b3 | C |  | add x1, x2, x4 | 
4 | fff08093 | 10 |  | addi x1, x1, -1 | Struct.,WAW(with 0xC)
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | 
7 | 01402383 | 1C |  | lw x7, 20(x0) | Done at the same time Write respectively
8 | 402200b3 | 20 |  | sub x1, x4, x2 | done at the same time
9 | ffd50093 | 24 |  | addi x1, x10,-3 | 
10 | 00520c63 | 28 |  | beq x4,x5,label0 | 
11 | 00420a63 | 2C |  | beq x4,x4,label0 | 
12 | 00000013 | 30 |  | addi x0, x0, 0 | not executed
13 | 00000013 | 34 |  | addi x0, x0, 0 | not executed
14 | 00000013 | 38 |  | addi x0, x0, 0 | not executed

## Slide 8: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 00000013 | 3C |  | addi x0, x0, 0 | not executed
16 | 000040b7 | 40 | label0: | lui x1, 4 | 
17 | 00c000ef | 44 |  | jal x1, 12 | WAW(with 0x40)
18 | 00000013 | 48 |  | addi x0, x0, 0 | not executed
19 | 00000013 | 4C |  | addi x0, x0, 0 | not executed
20 | ffff0097 | 50 |  | auipc x1, 0xffff0 | 
21 | 0223c433 | 54 |  | div x8, x7, x2 | 
22 | 025204b3 | 58 |  | mul x9, x4, x5 | 
23 | 022404b3 | 5C |  | mul x9, x8, x2 | Struct.,WAW(58);RAW(54)
24 | 00400113 | 60 |  | addi x2, x0, 4 | WAR(with 0x5C)
25 | 000000e7 | 64 |  | jalr x1, 0(x0) | 
26 | 00000013 | 68 |  | addi x0, x0, 0 | not executed
27 | 00000013 | 6C |  | addi x0, x0, 0 | not executed

## Slide 9: Actual Completion Sequence
NO. | Addr | ASM | Comment
0 | 0 | addi x0, x0, 0 | 
1 | 4 | lw x2, 4(x0) | x2=0x8
2 | 8 | lw x4, 8(x0) | x4=0x10
3 | C | add x1, x2, x4 | x1=0x18
4 | 10 | addi x1, x1, -1 | x1=0x17
5 | 14 | lw x5, 12(x0) | x5=0x14
6 | 18 | lw x6, 16(x0) | x6=0xFFFF0000
7 | 20 | sub x1, x4, x2 | x1=0x8
8 | 1C | lw x7, 20(x0) | x7=0x0FFF0000
9 | 24 | addi x1, x10,-3 | x1=0xFFFFFFFD
10 | 28 | beq x4,x5,label0 | no jump
11 | 2C | beq x4,x4,label0 | jump to 0x40
12 | 40 | lui x1, 4 | x1=0x4000
13 | 44 | jal x1, 12 | x1=0x48
14 | 50 | auipc x1, 0xffff0 | x1=FFFF0050

## Slide 10: Actual Completion Sequence
NO. | Addr | ASM | Comment
15 | 58 | mul x9, x4, x5 | x9=0x140
16 | 64 | jalr x1, 0(x0) | x1=0x68
17 | 54 | div x8, x7, x2 | x8=0x01FFE000
18 | 60 | addi x2, x0, 4 | x2=0x4
19 | 5C | mul x9, x8, x2 | x9=0x0FFF0000
15：54的除法需要计算36周期，时间较久，进入EX阶段之后不会马上结束。58的乘法issue后，5C的乘法由于结构竞争无法issue，直到58执行结束。因此第一条执行结束写回结果的是58。
16：58执行结束后，5C、60依次issue，但5C需要等待54的结果x8，暂时无法执行。60与5C在x2上存在WAR，因此在5C读取x2进入EX阶段之前也不能写结果。所以，目前存在“60写x2→5C读x2、x8→54写x8”的等待关系，在54结束之前5C、60都无法完成。64没有上述问题，因此正常issue后第二个完成。
17：64使得控制流跳转，从代码开头开始执行，但其第一条指令就是需要用到ALU的，因此与60产生结构竞争，无法issue。由于指令只能依次issue，执行就卡在这里，直到54执行完成。
18：54执行完成之后，5C读x2、x8进入EX阶段，此时60就可以写回x2了。
19：最后经过几个周期的计算，5C也写回其计算结果。

## Slide 11: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 12: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 13: Simulation (1)

## Slide 14: Simulation (2)

## Slide 15: Simulation (3)

## Slide 16: Simulation (4)

## Slide 17: Simulation (5)

## Slide 18: Simulation (6)

## Slide 19: Simulation (7)

## Slide 20: Simulation (8)

## Slide 21: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 22
Thanks!